## Slide 1: What not to do in a contest
Trent Sampson
WIA Director for Awards and Contests

## Slide 2: #1 Don’t read the rules
Contest managers change rules regularly
Obtain extra info on how to read them
Talk to contesters
VKCC Forum is one of the best
Watch out for the jargon

## Slide 3: Jargon
SO2R | Single Operator Two Radio
Multi Op | Multiple Operators
SOAB | Single Operator All Band
Mult | Multiplier
Dupe | Duplicate Contact
Rate | Contacts over a period

## Slide 4: Rules Change example
2011 CQ WPX
Multi Single was one transmitter
However one other transmitter could be used on another band if the contact(s) was with a new multiplier
2012 CQ WPX
Multi Single is one transmitter
No other transmitters can be used.
Seen as a dumbing down by many

## Slide 5: WPX Changes
No longer a need for “better technology”
Filtering ,TX lockouts not needed
Makes the contest purely a rate chase
Switch to the band with the highest rates into stronger areas and continue to build multipliers
Concentrate USA JA fast ops lots of multipliers

## Slide 6: Multipliers – How they work
QSO | Band | Band Points | Multiplier | QXBPXM
50 | 80 | 3 | 20 | 3000
100 | 40 | 2 | 20 | 4000
250 | 20 | 1 | 20 | 5000
250 | 15 | 2 | 20 | 10000
250 | 10 | 3 | 20 | 15000
 |  |  |  | 37000

## Slide 7: #2 Only have one antenna option
Less confusing
Easier to workout band changes
Saves mucking around working lots of stations
Keeps everything under control

## Slide 8: Terrain Analysis
Note: low take off angles missed by Red Curve

## Slide 9: Simple VK Contest Weapon
Thinking 80M
How do you cover all of VK ?
How do you do it consistently ?
Is there a better way ?
Where is the best location ?

## Slide 10: Coax Phasing Network
Simple to build
  Coax Switch
  3 Coax Tees
  2 X ¼ wavelength 70 ohm
  1 X ¼ wavelength 50 ohm
Transmitter always sees 50 ohms with 1 or both antennas
Single band only
More details at www.w9xt.com
Notes: Normally used to stack mono-band Yagis. L1, L2 must be same length
Can be used with different antenna types, L1, L2 any length

## Slide 11: Phasing Network

## Slide 12
Two special cases are at work here. A ¼ λ feed line will convert an open circuit on one end to a short circuit at the other. The inverse is true, and a short circuit on one end will appear as an open circuit at the other end. The other special case is that a ¼ λ 70 Ω coax will transform 50 Ω on one end to 100 Ω on the other.
Looking at the diagram, the switch is in the center position. In this position, both antennas will be connected. Antenna 1 will present a 50 Ω load at Tee connector A. The 70 Ω coax between connectors A and B will transform the 50 Ω to 100 Ω at connector B. Similarly, the impedance from Antenna 2 will also appear as 100 Ω at connector B. The two 100 Ω impedances in parallel form 50 Ω which is preserved through the 50 Ω coax back to the switch and to the transmitter

## Slide 13: VK Contests v International
VK
Tend not to use multipliers
Slower paced ease into
Band changes nice
Casual exchange “g’day Fred” “morning Ralph”
Repeat contacts allowed
Others
Multipliers
Face paced, expect pileups
Band changes critical
Exchange brief Report and go
No repeat contacts

## Slide 14: VK4SN and VK4NDX

## Slide 15: Software
Writelog – CW Decoder ,SSB,CW,RTTY
N1MM-SSB,CW,RTTY –Does VK (VK4SN)
Win Test – QSY Wizard super
VKCL – VK Contests very well Keyer options
RTTY (different strokes) MMTTY RTTY

## Slide 16: Simple Interfaces
RS232 DTR or RTS Lines, Audio in out, PTT Jaycar Microphone preamp kit to suit Heil

## Slide 17: Complicated Interfaces

## Slide 18: MK2R+

## Slide 19: Go Portable VK4NM@StGeorge QLD

## Slide 20: VK4TS 15M Yagi

## Slide 21: VK4UC
2 element Force 12 40M Beam 6M length Chromolly C31XR Tri-bander, Rippletech Sloper for 160/80
John VK4UC Heil Headset Micro-ham interface,K3, K500 Amp, Win-test, Six Pack

## Slide 22: #3 Operating
Talk as fast as you can
Never repeat your call-sign
Call every one over a wide spread
Never repeat your report for anyone
Never confirm the other call

## Slide 23: best of the best
480 VP2E N5TJ CQWWSSB2004 (qrate hour) update:2004-11-08 480 VP2KC JA3ODC CQWWSSB1979 update:2010-04-20 464 VP2E N5TJ CQWWSSB2003 (qrate hour) 460 WP3R K9PG ARRLSSB 2003 (qrate hour) 457 P40L N5TJ CQWWSSB 1993 430 ZF2MM K9PG ARRLSSB 2002 (qrate hour) 422 8P1A W2SC CQWWSSB 2003 (clock hour) 417 PJ2T K1AR CQWWSSB 2003 (clock hour) 409 ZF2NT K9PG ARRLSSB 2001 (qrate hour) 394 RC0F RC0F CQWWSSB 2011 (clock hour) update:2011-11-01 393 8P8P NN1N CQWWSSB 2002 (qrate hour, 10m) update:2004-08-31 392 NP4A K5ZD CQWWSSB 1981 (qrate hour)

## Slide 24: K9PG
gives his call-sign very regularly
Confirms the other calls
Is very brief
Can handle multiple calls
Different for intra VK Contests
Only in terms of not being brief

## Slide 25: #4 Setting up
Disable ALC
Increase Processor to +40
Warn the neighbours of severe solar electrical storm that will cause TV / stereo interference
Increase mike gain to the stopper
Send family away for weekend

## Slide 26: Best Practices
Read rules and under stand them
Align the rig and amps to manufacturer specs
Find the best location
Match antenna to location
Use Software for contest
Use Voice Keyers or CW keyers to reduce tiredness
Use a comfortable operating position

## Slide 27
Join the VKCC (free)
Come to the Dinner tonight
Enjoy today
Enter the next contest

## Slide 28: QUESTIONS

## Slide 29: Thank you